## Slide 1: Chapter 3
Arithmetic for Computers

## Slide 2: Arithmetic for Computers
Operations on integers
  Addition and subtraction
  Multiplication and division
  Dealing with overflow
Floating-point real numbers
  Representation and operations
§3.1 Introduction

## Slide 3: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0

## Slide 4: Integer Subtraction
Add negation of second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two +ve or two –ve operands, no overflow
  Subtracting +ve from –ve operand
    Overflow if result sign is 0
  Subtracting –ve from +ve operand
    Overflow if result sign is 1

## Slide 5: Arithmetic for Multimedia
Graphics and media processing operates on vectors of 8-bit and 16-bit data
  Use 64-bit adder, with partitioned carry chain
    Operate on 8×8-bit, 4×16-bit, or 2×32-bit vectors
  SIMD (single-instruction, multiple-data)
Saturating operations
  On overflow, result is largest representable value
    c.f. 2s-complement modulo arithmetic
  E.g., clipping in audio, saturation in video

## Slide 6: Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication

## Slide 7: Multiplication Hardware
Initially 0

## Slide 8: Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low

## Slide 9: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 10: RISC-V Multiplication
Four multiply instructions:
  mul: multiply
    Gives the lower 64 bits of the product
  mulh: multiply high
    Gives the upper 64 bits of the product, assuming the operands are signed
  mulhu: multiply high unsigned
    Gives the upper 64 bits of the product, assuming the operands are unsigned
  mulhsu: multiply high signed/unsigned
    Gives the upper 64 bits of the product, assuming one operand is signed and the other unsigned
  Use mulh result to check for 64-bit overflow

## Slide 11: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor
§3.4 Division

## Slide 12: Division Hardware
Initially dividend
Initially divisor in left half

## Slide 13: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both

## Slide 14: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT devision) generate multiple quotient bits per step
  Still require multiple steps

## Slide 15: RISC-V Division
Four instructions:
  div, rem: signed divide, remainder
  divu, remu: unsigned divide, remainder
Overflow and division-by-zero don’t produce errors
  Just return defined results
  Faster for the common case of no error

## Slide 16: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized
§3.5 Floating Point

## Slide 17: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 18: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 19: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 20: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 21: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 22: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 23: Floating-Point Example
What number is represented by the single-precision float
11000000101000…00
  S = 1
  Fraction = 01000…002
  Fxponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0

## Slide 24: Denormal Numbers
Exponent = 000...0  hidden bit is 0
Smaller than normal numbers
  allow for gradual underflow, with diminishing precision
Denormal with fraction = 000...0
Two representations of 0.0!

## Slide 25: Infinities and NaNs
Exponent = 111...1, Fraction = 000...0
  ±Infinity
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, Fraction ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0
  Can be used in subsequent calculations

## Slide 26: Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102

## Slide 27: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625

## Slide 28: FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 29: FP Adder Hardware
Step 1
Step 2
Step 3
Step 4

## Slide 30: Floating-Point Multiplication
Consider a 4-digit decimal example
  1.110 × 1010 × 9.200 × 10–5
1. Add exponents
  For biased exponents, subtract bias from sum
  New exponent = 10 + –5 = 5
2. Multiply significands
  1.110 × 9.200 = 10.212  10.212 × 105
3. Normalize result & check for over/underflow
  1.0212 × 106
4. Round and renormalize if necessary
  1.021 × 106
5. Determine sign of result from signs of operands
  +1.021 × 106

## Slide 31: Floating-Point Multiplication
Now consider a 4-digit binary example
  1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)
1. Add exponents
  Unbiased: –1 + –2 = –3
  Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127
2. Multiply significands
  1.0002 × 1.1102 = 1.1102  1.1102 × 2–3
3. Normalize result & check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4. Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5. Determine sign: +ve × –ve  –ve
  –1.1102 × 2–3 = –0.21875

## Slide 32: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP  integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 33: FP Instructions in RISC-V
Separate FP registers: f0, …, f31
  double-precision
  single-precision values stored in the lower 32 bits
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  flw, fld
  fsw, fsd

## Slide 34: FP Instructions in RISC-V
Single-precision arithmetic
  fadd.s, fsub.s, fmul.s, fdiv.s, fsqrt.s
    e.g., fadds.s f2, f4, f6
Double-precision arithmetic
  fadd.d, fsub.d, fmul.d, fdiv.d, fsqrt.d
    e.g., fadd.d f2, f4, f6
Single- and double-precision comparison
  feq.s, flt.s, fle.s
  feq.d, flt.d, fle.d
  Result is 0 or 1 in integer destination register
    Use beq, bne to branch on comparison result
Branch on FP condition code true or false
  B.cond

## Slide 35: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in f10, result in f10, literals in global memory space
Compiled RISC-V code:
f2c:
flw f0,const5(x3) // f0 = 5.0f
flw f1,const9(x3) // f1 = 9.0f
fdiv.s f0, f0, f1 // f0 = 5.0f / 9.0f
flw f1,const32(x3) // f1 = 32.0f
fsub.s f10,f10,f1 // f10 = fahr – 32.0
fmul.s f10,f0,f10 // f10 = (5.0f/9.0f) * (fahr–32.0f)
jalr x0,0(x1) // return

## Slide 36: FP Example: Array Multiplication
C = C + A × B
  All 32 × 32 matrices, 64-bit double-precision elements
C code:
void mm (double c[][], double a[][], double b[][]) { size_t i, j, k; for (i = 0; i < 32; i = i + 1) for (j = 0; j < 32; j = j + 1) for (k = 0; k < 32; k = k + 1) c[i][j] = c[i][j] + a[i][k] * b[k][j]; }
  Addresses of c, a, b in x10, x11, x12, and i, j, k in x5, x6, x7

## Slide 37: FP Example: Array Multiplication
RISC-V code:
mm:...
li x28,32 // x28 = 32 (row size/loop end)
li x5,0 // i = 0; initialize 1st for loop
L1: li x6,0 // j = 0; initialize 2nd for loop
L2: li x7,0 // k = 0; initialize 3rd for loop
slli x30,x5,5 // x30 = i * 2**5 (size of row of c)
add x30,x30,x6 // x30 = i * size(row) + j
slli x30,x30,3 // x30 = byte offset of [i][j]
add x30,x10,x30 // x30 = byte address of c[i][j]
fld f0,0(x30) // f0 = c[i][j]
L3: slli x29,x7,5 // x29 = k * 2**5 (size of row of b)
add x29,x29,x6 // x29 = k * size(row) + j
slli x29,x29,3 // x29 = byte offset of [k][j]
add x29,x12,x29 // x29 = byte address of b[k][j]
fld f1,0(x29) // f1 = b[k][j]

## Slide 38: FP Example: Array Multiplication
…
slli x29,x5,5 // x29 = i * 2**5 (size of row of a)
add x29,x29,x7 // x29 = i * size(row) + k
slli x29,x29,3 // x29 = byte offset of [i][k]
add x29,x11,x29 // x29 = byte address of a[i][k]
fld f2,0(x29) // f2 = a[i][k]
fmul.d f1, f2, f1 // f1 = a[i][k] * b[k][j]
fadd.d f0, f0, f1 // f0 = c[i][j] + a[i][k] * b[k][j]
addi x7,x7,1 // k = k + 1
bltu x7,x28,L3 // if (k < 32) go to L3
fsd f0,0(x30) // c[i][j] = f0
addi x6,x6,1 // j = j + 1
bltu x6,x28,L2 // if (j < 32) go to L2
addi x5,x5,1 // i = i + 1
bltu x5,x28,L1 // if (i < 32) go to L1

## Slide 39: Accurate Arithmetic
IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
  Choice of rounding modes
  Allows programmer to fine-tune numerical behavior of a computation
Not all FP units implement all options
  Most programming languages and FP libraries just use defaults
Trade-off between hardware complexity, performance, and market requirements

## Slide 40: Subword Parallellism
Graphics and audio applications can take advantage of performing simultaneous operations on short vectors
  Example: 128-bit adder:
    Sixteen 8-bit adds
    Eight 16-bit adds
    Four 32-bit adds
Also called data-level parallelism, vector parallelism, or Single Instruction, Multiple Data (SIMD)
§3.6 Parallelism and Computer Arithmetic: Subword Parallelism

## Slide 41: x86 FP Architecture
Originally based on 8087 FP coprocessor
  8 × 80-bit extended-precision registers
  Used as a push-down stack
  Registers indexed from TOS: ST(0), ST(1), …
FP values are 32-bit or 64 in memory
  Converted on load/store of memory operand
  Integer operands can also be converted on load/store
Very difficult to generate and optimize code
  Result: poor FP performance
§3.7 Real Stuff: Streaming SIMD Extensions and AVX in x86

## Slide 42: x86 FP Instructions
Optional variations
  I: integer operand
  P: pop operand from stack
  R: reverse operand order
  But not all combinations allowed
Data transfer | Arithmetic | Compare | Transcendental
FILD mem/ST(i) FISTP mem/ST(i) FLDPI FLD1 FLDZ | FIADDP mem/ST(i) FISUBRP mem/ST(i) FIMULP mem/ST(i) FIDIVRP mem/ST(i) FSQRT FABS FRNDINT | FICOMP FIUCOMP FSTSW AX/mem | FPATAN F2XMI FCOS FPTAN FPREM FPSIN FYL2X

## Slide 43: Streaming SIMD Extension 2 (SSE2)
Adds 4 × 128-bit registers
  Extended to 8 registers in AMD64/EM64T
Can be used for multiple FP operands
  2 × 64-bit double precision
  4 × 32-bit double precision
  Instructions operate on them simultaneously
    Single-Instruction Multiple-Data

## Slide 44: Matrix Multiply
Unoptimized code:
1. void dgemm (int n, double* A, double* B, double* C)
2. {
3. for (int i = 0; i < n; ++i)
4. for (int j = 0; j < n; ++j)
5. {
6. double cij = C[i+j*n]; /* cij = C[i][j] */
7. for(int k = 0; k < n; k++ )
8. cij += A[i+k*n] * B[k+j*n]; /* cij += A[i][k]*B[k][j] */
9. C[i+j*n] = cij; /* C[i][j] = cij */
10. }
11. }
§3.8 Going Faster: Subword Parallelism and Matrix Multiply

## Slide 45: Matrix Multiply
Optimized C code:
1. #include <x86intrin.h>
2. void dgemm (int n, double* A, double* B, double* C)
3. {
4. for (int i = 0; i < n; i+=8)
5. for (int j = 0; j < n; ++j)
6. {
7. __m512d c0 = _mm512_load_pd(C+i+j*n); // c0 = C[i][j]
8. for( int k = 0; k < n; k++ )
9. { // c0 += A[i][k]*B[k][j]
10. __m512d bb = _mm512_broadcastsd_pd(_mm_load_sd(B+j*n+k));
11. c0 = _mm512_fmadd_pd(_mm512_load_pd(A+n*k+i), bb, c0);
12. }
13. _mm512_store_pd(C+i+j*n, c0); // C[i][j] = c0
14. }
15.}

## Slide 46: Matrix Multiply
Optimized x86 assembly code:
vmovapd (%r11),%zmm1 | # Load 8 elements of C into %zmm1
mov %rbx,%rcx | # register %rcx = %rbx
xor %eax,%eax | # register %eax = 0
vbroadcastsd (%rax,%r8,8),%zmm0 | # Make 8 copies of B element in %zmm0
add $0x8,%rax | # register %rax = %rax + 8
vfmadd231pd (%rcx),%zmm0,%zmm1 | # Parallel mul & add %zmm0, %zmm1
add %r9,%rcx | # register %rcx = %rcx
cmp %r10,%rax | # compare %r10 to %rax
jne 50 <dgemm+0x50> | # jump if not %r10 != %rax
add $0x1, %esi | # register % esi = % esi + 1
vmovapd %zmm1, (%r11) | # Store %zmm1 into 8 C elements

## Slide 47: Right Shift and Division
Left shift by i places multiplies an integer by 2i
Right shift divides by 2i?
  Only for unsigned integers
For signed integers
  Arithmetic right shift: replicate the sign bit
  e.g., –5 / 4
    111110112 >> 2 = 111111102 = –2
    Rounds toward –∞
  c.f. 111110112 >>> 2 = 001111102 = +62
§3.9 Fallacies and Pitfalls

## Slide 48: Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
Need to validate parallel programs under varying degrees of parallelism

## Slide 49: Who Cares About FP Accuracy?
Important for scientific code
  But for everyday consumer use?
    “My bank balance is out by 0.0002¢!” 
The Intel Pentium FDIV bug
  The market expects accuracy
  See Colwell, The Pentium Chronicles

## Slide 50: Concluding Remarks
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs
§3.10 Concluding Remarks

## Slide 51: Concluding Remarks
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to reals
Bounded range and precision
  Operations can overflow and underflow