## Slide 1: Chapter 5
Large and Fast: Exploiting Memory Hierarchy

## Slide 2: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data
§5.1 Introduction

## Slide 3: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU

## Slide 4: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level

## Slide 5: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $500 – $1000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $3 – $6 per GB
Magnetic disk
  5ms – 20ms, $0.01 – $0.02 per GB
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk
§5.2 Memory Technologies

## Slide 6: DRAM Technology
Data stored as a charge in a capacitor
  Single transistor used to access the charge
  Must periodically be refreshed
    Read contents and write back
    Performed on a DRAM “row”

## Slide 7: Advanced DRAM Organization
Bits in a DRAM are organized as a rectangular array
  DRAM accesses an entire row
  Burst mode: supply successive words from a row with reduced latency
Double data rate (DDR) DRAM
  Transfer on rising and falling clock edges
Quad data rate (QDR) DRAM
  Separate DDR inputs and outputs

## Slide 8: DRAM Generations
Year | Capacity | $/GB
1980 | 64 Kibibit | $6,480,000
1983 | 256 Kibibit | $1,980,000
1985 | 1 Mebibit | $720,000
1989 | 4 Mebibit | $128,000
1992 | 16 Mebibit | $30,000
1996 | 64 Mebibit | $9,000
1998 | 128 Mebibit | $900
2000 | 256 Mebibit | $840
2004 | 512 Mebibit | $150
2007 | 1 Gibibit | $40
2010 | 2 Gibibit | $13
2012 | 4 Gibibit | $5
2015 | 8 Gibibit | $7
2018 | 16 Gibibit | $6

## Slide 9: DRAM Performance Factors
Row buffer
  Allows several words to be read and refreshed in parallel
Synchronous DRAM
  Allows for consecutive accesses in bursts without needing to send each address
  Improves bandwidth
DRAM banking
  Allows simultaneous access to multiple DRAMs
  Improves bandwidth

## Slide 10: Increasing Memory Bandwidth
4-word wide memory
  Miss penalty = 1 + 15 + 1 = 17 bus cycles
  Bandwidth = 16 bytes / 17 cycles = 0.94 B/cycle
4-bank interleaved memory
  Miss penalty = 1 + 15 + 4×1 = 20 bus cycles
  Bandwidth = 16 bytes / 20 cycles = 0.8 B/cycle

## Slide 11: Flash Storage
Nonvolatile semiconductor storage
  100× – 1000× faster than disk
  Smaller, lower power, more robust
  But more $/GB (between disk and DRAM)

## Slide 12: Flash Types
NOR flash: bit cell like a NOR gate
  Random read/write access
  Used for instruction memory in embedded systems
NAND flash: bit cell like a NAND gate
  Denser (bits/area), but block-at-a-time access
  Cheaper per GB
  Used for USB keys, media storage, …
Flash bits wears out after 1000’s of accesses
  Not suitable for direct RAM or disk replacement
  Wear leveling: remap data to less used blocks

## Slide 13: Disk Storage
Nonvolatile, rotating magnetic storage

## Slide 14: Disk Sectors and Access
Each sector records
  Sector ID
  Data (512 bytes, 4096 bytes proposed)
  Error correcting code (ECC)
    Used to hide defects and recording errors
  Synchronization fields and gaps
Access to a sector involves
  Queuing delay if other accesses are pending
  Seek: move the heads
  Rotational latency
  Data transfer
  Controller overhead

## Slide 15: Disk Access Example
Given
  512B sector, 15,000rpm, 4ms average seek time, 100MB/s transfer rate, 0.2ms controller overhead, idle disk
Average read time
  4ms seek time + ½ / (15,000/60) = 2ms rotational latency + 512 / 100MB/s = 0.005ms transfer time + 0.2ms controller delay = 6.2ms
If actual average seek time is 1ms
  Average read time = 3.2ms

## Slide 16: Disk Performance Issues
Manufacturers quote average seek time
  Based on all possible seeks
  Locality and OS scheduling lead to smaller actual average seek times
Smart disk controller allocate physical sectors on disk
  Present logical sector interface to host
  SCSI, ATA, SATA
Disk drives include caches
  Prefetch sectors in anticipation of access
  Avoid seek and rotational delay

## Slide 17: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
§5.3 The Basics of Caches
How do we know if the data is present?
Where do we look?

## Slide 18: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits

## Slide 19: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 20: Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 21: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 22: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 23: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 24: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 25: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 26: Address Subdivision

## Slide 27: Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address = 1200/16 = 75
Block number = 75 modulo 64 = 11
Tag
Index
Offset
0
3
4
9
10
63
4 bits
6 bits
22 bits

## Slide 28: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
  Larger blocks  pollution
Larger miss penalty
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help

## Slide 29: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 30: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 31: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 32: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block
  Write around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block

## Slide 33: Example: Intrinsity FastMATH
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle
Split cache: separate I-cache and D-cache
  Each 16KB: 256 blocks × 16 words/block
  D-cache: write-through or write-back
SPEC2000 miss rates
  I-cache: 0.4%
  D-cache: 11.4%
  Weighted average: 3.2%

## Slide 34: Example: Intrinsity FastMATH

## Slide 35: Main Memory Supporting Caches
Use DRAMs for main memory
  Fixed width (e.g., 1 word)
  Connected by fixed-width clocked bus
    Bus clock is typically slower than CPU clock
Example cache block read
  1 bus cycle for address transfer
  15 bus cycles per DRAM access
  1 bus cycle per data transfer
For 4-word block, 1-word-wide DRAM
  Miss penalty = 1 + 4×15 + 4×1 = 65 bus cycles
  Bandwidth = 16 bytes / 65 cycles = 0.25 B/cycle

## Slide 36: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplifying assumptions:
§5.4 Measuring and Improving Cache Performance

## Slide 37: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster

## Slide 38: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 39: Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 40: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 41: Associative Cache Example

## Slide 42: Spectrum of Associativity
For a cache with 8 entries

## Slide 43: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 44: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 45: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 46: Set Associative Cache Organization

## Slide 47: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 48: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 49: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 50: Example (cont.)
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss
  Extra penalty = 500 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 51: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size

## Slide 52: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
    Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyse
  Use system simulation

## Slide 53: Interactions with Software
Misses depend on memory access patterns
  Algorithm behavior
  Compiler optimization for memory access

## Slide 54: Software Optimization via Blocking
Goal: maximize accesses to data before it is replaced
Consider inner loops of DGEMM:
for (int j = 0; j < n; ++j)
{
double cij = C[i+j*n];
for( int k = 0; k < n; k++ )
cij += A[i+k*n] * B[k+j*n];
C[i+j*n] = cij;
}

## Slide 55: DGEMM Access Pattern
C, A, and B arrays
older accesses
new accesses

## Slide 56: Cache Blocked DGEMM
1 #define BLOCKSIZE 32
2 void do_block (int n, int si, int sj, int sk, double *A, double
3 *B, double *C)
4 {
5 for (int i = si; i < si+BLOCKSIZE; ++i)
6 for (int j = sj; j < sj+BLOCKSIZE; ++j)
7 {
8 double cij = C[i+j*n];/* cij = C[i][j] */
9 for( int k = sk; k < sk+BLOCKSIZE; k++ )
10 cij += A[i+k*n] * B[k+j*n];/* cij+=A[i][k]*B[k][j] */
11 C[i+j*n] = cij;/* C[i][j] = cij */
12 }
13 }
14 void dgemm (int n, double* A, double* B, double* C)
15 {
16 for ( int sj = 0; sj < n; sj += BLOCKSIZE )
17 for ( int si = 0; si < n; si += BLOCKSIZE )
18 for ( int sk = 0; sk < n; sk += BLOCKSIZE )
19 do_block(n, si, sj, sk, A, B, C);
20 }

## Slide 57: Blocked DGEMM Access Pattern
Unoptimized
Blocked

## Slide 58: Dependability
Fault: failure of a component
  May or may not lead to system failure
Service accomplishment
Service delivered as specified
Service interruption
Deviation from specified service
Failure
Restoration
§5.5 Dependable Memory Hierarchy

## Slide 59: Dependability Measures
Reliability: mean time to failure (MTTF)
Service interruption: mean time to repair (MTTR)
Mean time between failures
  MTBF = MTTF + MTTR
Availability = MTTF / (MTTF + MTTR)
Improving Availability
  Increase MTTF: fault avoidance, fault tolerance, fault forecasting
  Reduce MTTR: improved tools and processes for diagnosis and repair

## Slide 60: The Hamming SEC Code
Hamming distance
  Number of bits that are different between two bit patterns
Minimum distance = 2 provides single bit error detection
  E.g. parity code
Minimum distance = 3 provides single error correction, 2 bit error detection

## Slide 61: Encoding SEC
To calculate Hamming code:
  Number bits from 1 on the left
  All bit positions that are a power 2 are parity bits
  Each parity bit checks certain data bits:

## Slide 62: Decoding SEC
Value of parity bits indicates which bits are in error
  Use numbering from encoding procedure
  E.g.
    Parity bits = 0000 indicates no error
    Parity bits = 1010 indicates bit 10 was flipped

## Slide 63: SEC/DEC Code
Add an additional parity bit for the whole word (pn)
Make Hamming distance = 4
Decoding:
  Let H = SEC parity bits
    H even, pn even, no error
    H odd, pn odd, correctable single bit error
    H even, pn odd, error in pn bit
    H odd, pn even, double error occurred
Note: ECC DRAM uses SEC/DEC with 8 bits protecting each 64 bits

## Slide 64: Virtual Machines
Host computer emulates guest operating system and machine resources
  Improved isolation of multiple guests
  Avoids security and reliability problems
  Aids sharing of resources
Virtualization has some performance impact
  Feasible with modern high-performance comptuers
Examples
  IBM VM/370 (1970s technology!)
  VMWare
  Microsoft Virtual PC
§5.6 Virtual Machines

## Slide 65: Virtual Machine Monitor
Maps virtual resources to physical resources
  Memory, I/O devices, CPUs
Guest code runs on native machine in user mode
  Traps to VMM on privileged instructions and access to protected resources
Guest OS may be different from host OS
VMM handles real I/O devices
  Emulates generic virtual I/O devices for guest

## Slide 66: Example: Timer Virtualization
In native machine, on timer interrupt
  OS suspends current process, handles interrupt, selects and resumes next process
With Virtual Machine Monitor
  VMM suspends current VM, handles interrupt, selects and resumes next VM
If a VM requires timer interrupts
  VMM emulates a virtual timer
  Emulates interrupt for VM when physical timer interrupt occurs

## Slide 67: Instruction Set Support
User and System modes
Privileged instructions only available in system mode
  Trap to system if executed in user mode
All physical resources only accessible using privileged instructions
  Including page tables, interrupt controls, I/O registers
Renaissance of virtualization support
  Current ISAs (e.g., x86) adapting

## Slide 68: Virtual Memory
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)
Programs share main memory
  Each gets a private virtual address space holding its frequently used code and data
  Protected from other programs
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault
§5.7 Virtual Memory

## Slide 69: Address Translation
Fixed-size pages (e.g., 4K)

## Slide 70: Page Fault Penalty
On page fault, the page must be fetched from disk
  Takes millions of clock cycles
  Handled by OS code
Try to minimize page fault rate
  Fully associative placement
  Smart replacement algorithms

## Slide 71: Page Tables
Stores placement information
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 72: Translation Using a Page Table

## Slide 73: Mapping Pages to Storage

## Slide 74: Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 75: Fast Translation Using a TLB
Address translation would appear to require extra memory references
  One to access the PTE
  Then the actual memory access
But access to page tables has good locality
  So use a fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)
  Typical: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software

## Slide 76: Fast Translation Using a TLB

## Slide 77: TLB Misses
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table
  Then restart the faulting instruction

## Slide 78: TLB Miss Handler
TLB miss indicates
  Page present, but PTE not in TLB
  Page not preset
Must recognize TLB miss before destination register overwritten
  Raise exception
Handler copies PTE from memory to TLB
  Then restarts instruction
  If page not present, page fault will occur

## Slide 79: Page Fault Handler
Use faulting virtual address to find PTE
Locate page on disk
Choose page to replace
  If dirty, write to disk first
Read page into memory and update page table
Make process runnable again
  Restart from faulting instruction

## Slide 80: TLB and Cache Interaction
If cache tag uses physical address
  Need to translate before cache lookup
Alternative: use virtual address tag
  Complications due to aliasing
    Different virtual addresses for shared physical address

## Slide 81: Memory Protection
Different tasks can share parts of their virtual address spaces
  But need to protect against errant access
  Requires OS assistance
Hardware support for OS protection
  Privileged supervisor mode (aka kernel mode)
  Privileged instructions
  Page tables and other state information only accessible in supervisor mode
  System call exception (e.g., ecall in RISC-V)

## Slide 82: The Memory Hierarchy
Common principles apply at all levels of the memory hierarchy
  Based on notions of caching
At each level in the hierarchy
  Block placement
  Finding a block
  Replacement on a miss
  Write policy
§5.8 A Common Framework for Memory Hierarchies
The BIG Picture

## Slide 83: Block Placement
Determined by associativity
  Direct mapped (1-way associative)
    One choice for placement
  n-way set associative
    n choices within a set
  Fully associative
    Any location
Higher associativity reduces miss rate
  Increases complexity, cost, and access time

## Slide 84: Finding a Block
Hardware caches
  Reduce comparisons to reduce cost
Virtual memory
  Full table lookup makes full associativity feasible
  Benefit in reduced miss rate
Associativity | Location method | Tag comparisons
Direct mapped | Index | 1
n-way set associative | Set index, then search entries within the set | n
Fully associative | Search all entries | #entries
 | Full lookup table | 0

## Slide 85: Replacement
Choice of entry to replace on a miss
  Least recently used (LRU)
    Complex and costly hardware for high associativity
  Random
    Close to LRU, easier to implement
Virtual memory
  LRU approximation with hardware support

## Slide 86: Write Policy
Write-through
  Update both upper and lower levels
  Simplifies replacement, but may require write buffer
Write-back
  Update upper level only
  Update lower level when block is replaced
  Need to keep more state
Virtual memory
  Only write-back is feasible, given disk write latency

## Slide 87: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size

## Slide 88: Cache Design Trade-offs
Design change | Effect on miss rate | Negative performance effect
Increase cache size | Decrease capacity misses | May increase access time
Increase associativity | Decrease conflict misses | May increase access time
Increase block size | Decrease compulsory misses | Increases miss penalty. For very large block size, may increase miss rate due to pollution.

## Slide 89: Cache Control
Example cache characteristics
  Direct-mapped, write-back, write allocate
  Block size: 4 words (16 bytes)
  Cache size: 16 KB (1024 blocks)
  32-bit byte addresses
  Valid bit and dirty bit per block
  Blocking cache
    CPU waits until access is complete
§5.9 Using a Finite-State Machine to Control A Simple Cache
Tag
Index
Offset
0
3
4
13
14
31
4 bits
10 bits
18 bits

## Slide 90: Interface Signals
Cache
CPU
Memory
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
32
32
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
128
128
Multiple cycles per access

## Slide 91: Finite State Machines
Use an FSM to sequence control steps
Set of states, transition on each clock edge
  State values are binary encoded
  Current state stored in a register
  Next state = fn (current state, current inputs)
Control output signals = fo (current state)

## Slide 92: Cache Controller FSM
Could partition into separate states to reduce clock cycle time

## Slide 93: Cache Coherence Problem
Suppose two CPU cores share a physical address space
  Write-through caches
§5.10 Parallelism and Memory Hierarchies: Cache Coherence
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
3 | CPU A writes 1 to X | 1 | 0 | 1

## Slide 94: Coherence Defined
Informally: Reads return most recently written value
Formally:
  P writes X; P reads X (no intervening writes)  read returns written value
  P1 writes X; P2 reads X (sufficiently later)  read returns written value
    c.f. CPU B reading X after step 3 in example
  P1 writes X, P2 writes X  all processors see writes in the same order
    End up with the same final value for X

## Slide 95: Cache Coherence Protocols
Operations performed by caches in multiprocessors to ensure coherence
  Migration of data to local caches
    Reduces bandwidth for shared memory
  Replication of read-shared data
    Reduces contention for access
Snooping protocols
  Each cache monitors bus reads/writes
Directory-based protocols
  Caches and memory record sharing status of blocks in a directory

## Slide 96: Invalidating Snooping Protocols
Cache gets exclusive access to a block when it is to be written
  Broadcasts an invalidate message on the bus
  Subsequent read in another cache misses
    Owning cache supplies updated value
CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
 |  |  |  | 0
CPU A reads X | Cache miss for X | 0 |  | 0
CPU B reads X | Cache miss for X | 0 | 0 | 0
CPU A writes 1 to X | Invalidate for X | 1 |  | 0
CPU B read X | Cache miss for X | 1 | 1 | 1

## Slide 97: Memory Consistency
When are writes seen by other processors
  “Seen” means a read returns the written value
  Can’t be instantaneously
Assumptions
  A write completes only when all processors have seen it
  A processor does not reorder writes with other accesses
Consequence
  P writes X then writes Y  all processors that see new Y also see new X
  Processors can reorder reads, but not writes

## Slide 98: Multilevel On-Chip Caches
§5.13 The ARM Cortex-A53 and Intel Core i7 Memory Hierarchies

## Slide 99: 2-Level TLB Organization

## Slide 100: Supporting Multiple Issue
Both have multi-banked caches that allow multiple accesses per cycle assuming no bank conflicts
Other optimizations
  Return requested word first
  Non-blocking cache
    Hit under miss
    Miss under miss
  Data prefetching

## Slide 101: RISC-V System Instructions
§5.14 Real Stuff: RISC-V System and Special Instructions
Type | Mnemonic | Name
Mem ordering | fence.i | Instruction fence
 | fence | Fence
 | sfence.vm | Address translation fence
CSR access | csrrwi | CSR read/write immediate
 | csrrsi | CSR read/set immediate
 | csrrci | CSR read/clear immediate
 | csrrw | CSR read/write
 | csrrs | CSR read/set
 | csrrc | CSR read/clear
System | ecall | Environment call
 | ebreak | Environment breakpoint
 | sret | Supervisor exception return
 | wfi | Wait for interrupt

## Slide 102: DGEMM
Combine cache blocking and subword parallelism
§5.15 Going Faster: Cache Blocking and Matrix Multiply

## Slide 103: Pitfalls
Byte vs. word addressing
  Example: 32-byte direct-mapped cache, 4-byte blocks
    Byte 36 maps to block 1
    Word 36 maps to block 4
Ignoring memory system effects when writing or generating code
  Example: iterating over rows vs. columns of arrays
  Large strides result in poor locality
§5.16 Fallacies and Pitfalls

## Slide 104: Pitfalls
In multiprocessor with shared L2 or L3 cache
  Less associativity than cores results in conflict misses
  More cores  need to increase associativity
Using AMAT to evaluate performance of out-of-order processors
  Ignores effect of non-blocked accesses
  Instead, evaluate performance by simulation

## Slide 105: Pitfalls
Extending address range using segments
  E.g., Intel 80286
  But a segment is not always big enough
  Makes address arithmetic complicated
Implementing a VMM on an ISA not designed for virtualization
  E.g., non-privileged instructions accessing hardware resources
  Either extend ISA, or require guest OS not to use problematic instructions

## Slide 106: Concluding Remarks
Fast memories are small, large memories are slow
  We really want fast, large memories 
  Caching gives this illusion 
Principle of locality
  Programs use a small part of their memory space frequently
Memory hierarchy
  L1 cache  L2 cache  …  DRAM memory  disk
Memory system design is critical for multiprocessors
§5.17 Concluding Remarks